## Slide 1: FTC Programming Class

## Slide 2: What is FTC?
First Tech Challenge is a STEM program for students to learn about technology in an applied setting.
There are multiple elements to the overall program:
  FTC teams design, build (and program!) robots to compete with other teams
  Community outreach
  Management of the business aspects and documentation of the processes

## Slide 3: Match Tasks
Each new season has a set of specific tasks.
Each match always has the same two sessions:
  Autonomous (30 seconds long)
    Robot is started, and accomplishes the tasks on its own with no driver intervention
  Teleop (2 minutes, 30 seconds long)
    Drivers operate the robot to accomplish tasks

## Slide 4: Typical Tasks
Motion – Robot moves/is driven
Localization/Navigation – Robot goes to a specific spot on field
Recognition – Robot needs to identify certain objects, and tailor program accordingly
Gathering/Intake – Robot acquires game elements
Lifting – Robot selects and moves game elements
Launching – Robot shoots game elements
Placing – Robot places game elements
Latching – Robot affixes to game elements to move them

## Slide 5: FTC Programming
FTC uses Android devices for the base program platform
The fundamental programming language is Java
There are three “official” development environments:
  Blocks
  Onbot Java
  Android Studio

## Slide 6: Blocks Language
Blocks is a interface that allows you to program a robot without learning Java
Pros:
  Start programming quickly
  Do not need to learn Java
Cons:
  Difficult to do many more advanced tasks
  Slooooowwww interface!
    Large programs can be almost unusable

## Slide 7: Blocks Language

## Slide 8: OnBot Java
Onbot Java is a simplified development tool, using actual Java language
  Pros:
    Easy to get up and running
    Easy for use with multiple programmers on team
    Easy to manage software
  Cons:
    Need to follow process to keep from losing or corrupting the program
    Difficult or impossible to do advanced programming features (like some vision programs)

## Slide 9: OnBot Java

## Slide 10: Android Studio
Android Studio is the professional IDE (Integrated Development Environment) used by programmers that write apps on Android phones
  Pros:
    Flexible
    Can write more advanced Java programs using Object Oriented Programming
  Cons:
    Hard to set up
    Not user friendly
    Very hard for multiple users

## Slide 11: TDT Coach Recommendation
Recommend OnBot Java for this season
  Need to learn some basics, but do not need to become experts
  Has the power to do what needs to be done
  Can reuse Java code from previous season

## Slide 12: Basic FTC Control Architecture

## Slide 13: Opmodes
Opmodes are the programs that control the robot
Two key types of opmodes:
  Linear Opmode:
    Used for Autonomous
    Runs through the program only once
  Iterative Opmode:
    Used for Teleop
    Runs as a continuous loop

## Slide 14: Typical Opmode Structure
Header (package imports)
Define Opmode (auto or teleop)
Name the Class
Declare hardware
Declare runopmode
Assign hardware
Set hardware attributes
Wait for Start
Main opmode loop

## Slide 15: Java Syntax
Individual statements must end in a semicolon (;)
Methods, loops and other items are bounded in brackets ({)
All bracketed items need to correspond with another bracket if nested

## Slide 16: Java Operators
Operators are used to test and assign statements and numbers
Sample operators:
  = (assignment)
  == (logical equal to)
  < (less than)
  && (logical AND)
  != (not equal to)
  ++ (increment by one)

## Slide 17: Data Types/Variables
Java has a wide range of data types
Variables are used to store values
Most common types are:
  int (smaller positive and negative whole numbers)
  double (larger positive and negative numbers)
  boolean (“true” and “false”)

## Slide 18: Example of variable usage
Declare the variable
  int dogs = 5;
  dogs = dogs +10;
  dogs = dogs +5;

## Slide 19: Conditional if/else
If/else is very powerful tool in programming
It is used to test if certain things have happened or not, and have the program react appropriately
Example:
if (test expression){
  do this thing
  }
  else {
  do something different
  }

## Slide 20: If/else example
int cats =0;
if (dogs ==20){
  cats = 50;
  }
  else {
  cats = 100;
  }

## Slide 21: Loops
Programs are loops
You can set up loops to control actions
Common loops;
  while loop
    Runs the loop until the test expression is false, then leaves loop
  for loop
    Runs the loop a specified number of times

## Slide 22: while loop example
dogs =0;
cats = 0;
while (dogs < 21){
cats = cats+2;
dogs = dogs +1;
}

## Slide 23: for loop example
dogs =0;
cats = 0;
public int loop1;
for (loop1=0; loop1 <21; loop1++){
cats = cats+2;
dogs = dogs +1;
}

## Slide 24: Motors
FTC motors are DC motors, and can run either in forward or reverse
You need to specify motor rotation in the hardware setup
  FORWARD
  REVERSE
The command setPower applies power to the motor to have it turn.
The range of setPower is -1 to 1.
  0 is no power, .5 is half power, 1 is full power

## Slide 25: Motor run modes
The Rev hub has different ways to control the motor running. There are three basic modes:
  RUN_WITHOUT_ENCODER
  RUN_USING_ENCODER
  RUN_TO_POSITION

## Slide 26: Motor run modes
RUN_WITHOUT_ENCODER
  Simplest mode
  Applies raw battery power to motor
RUN_USING_ENCODER
  Uses the motor encoder to try to run to a certain speed
RUN_TO_POSITION
  Uses the motor encoder to turn the motor to a certain position

## Slide 27: Motor Encoders
Most FTC motors have built in encoders
Encoders provide feedback to the Rev hub in the form of “ticks”.
Motors have a specific number of ticks per revolution (for example 1000 ticks per revolution)

## Slide 28: Motor Encoders
Using the feedback from the encoders, we can make the robot move a specified distance.
Example:
  Suppose your robot wheel is connected direct to motor, and each motor revolution is 1000 ticks.
  Your robot wheel is 4 inches in diameter, so the circumference is πD, or 4 X 3.14 = 12.57 inches
  This means the robot should move 12.57 inches with every revolution of the motor
  1000/12.57 = 79.55 ticks per inch

## Slide 29: Simple code to move robot 5 inches
  5 inches x 79.55= 398 ticks
    (always use whole numbers with int data types!)
int ticks=0;
ticks = leftFront.getCurrentPosition();
while (ticks<398){
  leftFront.setPower(.5);
  rightFront.setPower(.5);
  leftBack.setPower(.5);
  rightBack.setPower(.5);
  }
  leftFront.setPower(0);
  rightFront.setPower(0);
  leftBack.setPower(0);
  rightBack.setPower(0);

## Slide 30: Odometry Encoders
Using motor encoders has a major problem: Wheel slippage
This causes inaccurate movement
To solve this, use of “dead wheels” with encoders.

## Slide 31: Telemetry
Programming can be very challenging
  You WILL have frustrating times when things don’t work like you think they should
Telemetry is very powerful tool to help you see what is really happening with your code
Inserting AddTelemetry and Update Telemetry commands in your code gives you feedback