## Slide 1: FTC Programming Class
Session 2

## Slide 2: Topics for today
Tasks (Revisited)
Planning for this Season
Java Classes and Methods
Telemetry
Turning the Robot- Using the IMU
Intro to Machine Learning

## Slide 3: Typical Tasks
Motion – Robot moves/is driven
Localization/Navigation – Robot goes to a specific spot on field
Recognition – Robot needs to identify certain objects, and tailor program accordingly
Gathering/Intake – Robot acquires game elements
Lifting – Robot selects and moves game elements
Launching – Robot shoots game elements
Placing – Robot places game elements
Latching – Robot affixes to game elements to move them

## Slide 4: Season Tasks Planning
Discussion/Objectives
Robot movements
Robot other actions
  Gripping object
  Placing objects
Always best to map out actions, write up pseudocode of what you want robot to do

## Slide 5: Classes
Classes are a powerful feature of Java
  Fundamental principle of Object Oriented Programming
Classes and objects are the two main aspects of object-oriented programming.
Example:
  Class = FRUIT
  Objects Banana, Apple, Orange
A class is a template for objects, and an object is an instance of a class
When the individual objects are created, they inherit all the variables and methods from the class
Onbot Java doesn’t handle OOP well, so we will focus on methods within the main class

## Slide 6: Methods
Methods in Java are functions that perform tasks
Extremely useful to achieve repetitive tasks with minimal code
Methods can accomplish three basic task types:
  Complete a task, and return a value
  Pass value(s) to the method to be acted on
  Do the task without either returning a value or needing any input

## Slide 7: Method Usage
Need to declare and define the method:
Return variable methodName(argument1, argumentx) {
task
}
Example from last season, simple:
public void setPowerZero(){
rightBack.setPower(0);
leftFront.setPower(0);
rightFront.setPower(0);
leftBack.setPower(0);
}
Usage:
setPowerZero();
public void setPowerZero(){ rightBack.setPower(0); leftFront.setPower(0); rightFront.setPower(0); leftBack.setPower(0); }

## Slide 8: Method Usage
More complex example from last season:
public int inchesToTicks(double inches) {
final double wheelDiameter = 2.8;
final double distancePerRevolution = wheelDiameter * Math.PI; //Inches
final double ticksPerRevolution = 1000;
return (int)(((inches) / distancePerRevolution) * ticksPerRevolution);
}

## Slide 9: Telemetry
Telemetry allows you to view program status and elements on the driver station phone
Extremely useful for debugging your program
  View contents of your variables
  Detect where you are in the program

## Slide 10: Telemetry Structure/Usage
Principle forms:
telemetry.addData(“Title", “string”); telemetry.update();
telemetry.addData(“Title", variable); telemetry.update();
telemetry.addData(“Title", method); telemetry.update();

## Slide 11: Telemetry Examples
String Example:
telemetry.addData("Status", "Initialized");
telemetry.update();
Variable Example:
telemetry.addData("Robot Angle", robotAngle);
telemetry.update();
Method Example:
telemetry.addData(“Right Dist”,rightDistance.getDistance(DistanceUnit.INCH));
telemetry.update();

## Slide 12: Turning the Robot
Simplest way to turn the Robot = Tank Drive
  To turn the robot Right:
    Rotate left side wheels FORWARD
    Rotate right side wheels REVERSE
  To turn the robot Left:
    Rotate left side wheels REVERSE
    Rotate right side wheels FORWARD
How can you turn the robot a certain amount (or to a certain angle?

## Slide 13: Possible ways to turn
Turn by applying alternate power a certain amount of time
  Not very accurate, no feedback for robot angle
Turn by applying alternate power for a certain number of wheel encoder ticks
  More accurate than power/time
  Angle & repeatability dependent on wheel slippage
  (Using odometry wheels improves accuracy)
Turn by using internal gyroscope (Integrated Measurement Unit)
  Most accurate method
  Turn until reach a target angle

## Slide 14: The IMU
Built-in function of the Rev Hub
Can measure X Y and Z angles of robot
  Normally only use for robot rotation
General principle for using IMU for checking rotation angle:
  Initialize the IMU at start of program:
    BNO055IMU.Parameters imuParameters;
    Orientation angles;
    imuParameters = new BNO055IMU.Parameters();
    imuParameters.angleUnit = BNO055IMU.AngleUnit.DEGREES;
    imuParameters.loggingEnabled = false;
    imu.initialize(imuParameters);
    angles = imu.getAngularOrientation(AxesReference.INTRINSIC, AxesOrder.ZYX, AngleUnit.DEGREES);
    robotAngle = angles.firstAngle;
  Query IMU to report current angle:
    angles = imu.getAngularOrientation(AxesReference.INTRINSIC, AxesOrder.ZYX, AngleUnit.DEGREES);
    robotAngle =angles.firstAngle;

## Slide 15: Quirks of the IMU
Clockwise (right) turns to 180 degrees are negative numbers!
  A right turn to 90 degrees is to turn to -90 degrees
Counterclockwise (left) turns to 180 degrees are positive numbers!
  A left turn to 90 degrees is to turn to 90 degrees
This makes programming a bit challenging…..

## Slide 16: Example Turn Code
robotAngle = 0; targetAngle = -179; while (!(targetAngle >=robotAngle )) { //while target angle is NOT greater than equal to bot angle, if negative switch it :) double PIDpwr = ((targetAngle - robotAngle) * 0.006) - .1; double left_pwr = PIDpwr * -1 ; double right_pwr = PIDpwr ; leftFront.setPower(left_pwr); leftBack.setPower(left_pwr); rightFront.setPower(right_pwr); rightBack.setPower(right_pwr); angles = imu.getAngularOrientation(AxesReference.INTRINSIC, AxesOrder.ZYX, AngleUnit.DEGREES); robotAngle =angles.firstAngle; if ((targetAngle < -90) && (robotAngle > 10)){ robotAngle = (robotAngle-360); } } setPowerZero();

## Slide 17: Basic Machine Learning
FTC games ALWAYS include aspects of visual recognitions
  Game elements recognition to do subsequent tasks
  Position targets on the field
2021 Season:
  Detect presence of zero, one, or 4 rings and perform tasks
2020 Season:
  Detect location of special game element (Skystone) and perform tasks
2019 Season:
  Detect location of Gold element and move it to specific location

## Slide 18: FTC ML Framework
FTC created basic framework for AI/ML and updates it for every year
Vuforia is the basic AI framework
  Vision detection and location in field of view
TensorFlow is the AI model Framework
  FTC creates TF models for specific game elements each year
Accuracy and reliability in the past has been an issue
  2019 ; Models were not built properly, lighting very dependent
  2020 ; Skystone image model also lighting dependent, needed to be very close to object
  2021 ; Best Season yet! (almost 100% reliability)

## Slide 19: New Season Challenge
New season provides new challenge:
  Team custom game element
  Need to identify location of custom element
FTC is ready to issue beta test for model-building software
  TDT has applied to participate in beta test

## Slide 20: TDT Custom Element
Past seasons have had team-custom game elements
Previous seasons requirements mainly resulted in teams created elements that they could store, grip, and place the easiest.
This season provides a new criteria:
  Ease of TensorFlow to recognize the element 100%