## Slide 1: FTC Programming Class
Session 3

## Slide 2: Topics for today
Using Servos
Using Distance Sensors
TensorFlow Beta – Implementation
Code Walkthrough

## Slide 3: Servos
Servos provide precise rotational movements, with limited total rotation
  Typically 180 degrees
(note, some servos can do continuous rotation, like a motor)

## Slide 4: Typical Servo Applications
Last year’s robot used two servos:
  The “Wobble Gripper” (servo opened and closed the wobble grip “hand”)
  The “Shooter Flicker” (servo pushed each ring in the shooter into the rotating wheel assembly)
Servos are ideal for small precise movements
  Smaller and lighter than motors

## Slide 5: Limitations of servos
Servos have some key limitations:
  Relatively slow movement speed
  Torque limitation – easily damaged
  Single-ended bearing – easily damaged

## Slide 6: Programming Servos
The entire range (about 180 degrees) of rotation on a servo is defined by numbers between 0 and 1.
For example, the mid-point of rotation is defined by a setting of .50
General steps to use a servo:
  Declare the servo at beginning:
    private Servo shooterServo;
  Initialize the servo:
    shooterServo = hardwareMap.servo.get("shooterServo");
  To rotate to mid point:
    shooterServo.setPosition(0.43);
private Servo shooterServo;

## Slide 7: Servo tips and tricks
Since servos are relatively slow, you may need to pause your next step in your robot action to allow time for the servo to move
  Example:
    wobbleServo.setPosition(.45); // Close wobble servo to release wobble
    sleep(150);
It is hard to remember what specific servo values mean in your application. It is best to define what it does as a variable, and use that in your code
  public double wgripOpen = .15;
  public double wgripClosed = .45;
  wobbleServo.setPosition(wgripClosed); // Close wobble servo to release wobble

## Slide 8: Distance Sensors
Function of a Distance Sensor:
  Measure and Report distance from the sensor to another object or wall
  Example: Last season, we used two sensors to pick up the second wobble goal
  One sensor measured the side distance to wall
  The other measured the front distance to wall
  Program moved robot to align robot with the location of the wobble using info from the distance sensor
General steps to use a distance sensor:
  Declare the distance sensor at beginning:
    ModernRoboticsI2cRangeSensor rightDistance;
  Initialize the sensor:
    rightDistance = hardwareMap.get(ModernRoboticsI2cRangeSensor.class, "rightDistance");
  To get distance:
    rightDist = rightDistance.getDistance(DistanceUnit.INCH);